## Slide 1: Meet_28_May
Found gps co-ordinates of a gmap route and created a complete virtual trip with obd parameters and location co-ordinates

## Slide 2: Meet 16_May
Learned about GPS Module and tried interfacing it with Arduino UNO
Performed Experiments and received values of longitude and latitude and also successfully opened google map location using those values
Tried to merge Gateway-GSM-GPS in ESP32 code, but there is some problem
Modified Study Phase and Design Phase in Thesis Report
While merging GSM module functionality in Gateway code, the code was not running well and there was a problem in sending http requests in ESP32
There was a problem using Software serial library with ESP32 and was not recommended to use as per internet sources, therefore the problem was solved by using Hardware serial setup instead of software serial setup. We can reconfigure the UART pins to any of GPIO pins using Hardware serial setup

## Slide 3
Designed a program to merge GSM and GPS, the location tracked from gps was converted to a gmap URL and then was sent through SMS to our phone.
Modified update_unsafe function in MongoDB Realm, now at the time of updating the Asset status as unsafe, last location where the Tag was connected will be updated.
Designed update_last_loc function in MongoDB Realm, which will be used by Gateway to update the last location received by GPS module.
Modified the post_bus function, now along with OBD parameters it will also store gmap location.
Planning to store g-map location in database once Tag gets disconnected, Also provide user to get current g-map location of Asset from App. This will be helpful for user who are not actually travelling but only sending some luggage from bus.
Imported a sample dataset containing OBD Data in MongoDB from a csv file

## Slide 4: Meet 2_May
As suggested in last meet, now OTP generation takes place at MongoDB and the app only sends Mobile number.
Added the feature of checking response code from web and re-initiating the process (post/get/delete) in case of any error. Earlier if there was a network problem or something, then also screen was changed without even showing error message
Also if the error remains after 3 attempts then display the error description based on the response code
Earlier there was a problem of keyboard appearing in front of textbox , removing the visibility . That problem has been resolved by making the screen-Arrangement as scrollable
Modified some tasks in app to work in a sequential manner. After previous task is completed then only button for next task is enabled and/or next task is triggered. As earlier there was a problem of verifying password in case of any delay in http response and user had to press connect button multiple times
We did research about OBD (added in slides)

## Slide 5: Meet 25_April
Learned about GSM Module
Programmed UNO and ESP32 to use GSM Module to send messages and make calls
Made separate collection for containing OTP data and designed various Realm functions for post, get and delete OTP related document in database
Modified user and conductor apps to work with OTP sending feature
Modified the earlier report and did plagiarism check in “Grammarly”

## Slide 6: Meet 11_April
The locking action of tag was set to occur in accordance with the “Lock_Status” key in “Lock Data” Database, which gets updated as 1 or 0 at time of adding or removing entry of passenger in database.
Modified MongoDB Realm Functions for updating values in integer form, required for preparing charts
Learnt about the Charts feature provided by MongoDB
Created a Dashboard in MongoDB Charts and created two charts in it for storing “Lock Status” and “Distance Travelled”
Completed an Experiment in which we transferred OBD data from app to Esp32 and then received via CAN Bus and uploaded in database “BUS_INFO” which was plotted in chart
GSM module part is pending
Next week : GSM module part, chart for other parameters, making the lock size small, Thesis preparation

## Slide 7: Meet 4_April
OBD Simulator part is completed. Now obd data changed in app are successfully visible in serial terminal.
Created a separate collection named “Lock_Data” in database
Added functions to update “Lock_Status” of tag in corresponding document
Trying to merge unlocking part at the time of removing an entry. Little bit work is remaining

## Slide 8: Meet 28_Mar
Programmed one ESP32 to work as OBD Simulator and received values sent from it in another ESP32
Designed OBD Simulator App to send Data values via Bluetooth to ESP32 Simulator. App has sliders to vary different parameters value
Little work is left in OBD part
Amit has completed Lock

## Slide 9: Meet 21_Mar
Button size adjusted in side menu
Added the contact update option in conductor app
CAN Bus communication between two ESP32 established
Trying to establish OBD in ESP32s using MCP2551 CAN Transceiver
Prepared Design Phase Report
Amit is working on lock part

## Slide 10: Meet 7_Mar
Amit is working on the lock part
Added the drop down menu for selection of beacon id in Query function in ble_conductor and in login screen of ble_user
Made the Query result expandable in conductor app
Added functionality to remove passenger entry from conductor app
Added side menu and home buttons in app
Prepared a user manual for both the apps
Will work on disconnection issue this week

## Slide 11: Meet 28_feb
Resolved the reconnection problem in Esp32
Added the remove entry functionality in apps and delete functionality in MongoDB realm functions
Decompiled the apk files and got the java codes for our apps
Amit is working on the lock part
Demo

## Slide 12: Meet 14_feb
The app uses http requests, therefore we will have to use encryption
Encryption feature available in MongoDB Enterprise version only
MongoDB Encryption will make the whole Realm Encrypted
We added Encryption Decryption in APP itself using Asymmetric Encryption method
Prepared Report and mailed Chezhyan sir
Read about OBD II

## Slide 13: Meet 7_feb
Found GSM-module products for Gateways
Reading about the Advanced Encryption Standard for encryption of data

## Slide 14: Meet 31_Jan
Solved the conductor app crashing problem
Designed the Forgot Password screen of Conductor
Partially Solved the beacon reconnection problem using software reset
Found a service provided by twilio to send messages
Tried to design the first programmable sms and to merge with MongoDB Realm Function, but attempt was unsuccessful

## Slide 15: Meet 24_Jan
Programmed one ESP32 to work as BLE Beacon and another to work as a BLE Gateway.
Added the functionality of tracking the beacon and merged the updating of Status in MongoDB
Whenever the Beacon gets disconnected due to large Distance, it updates the Asset Status of entry with Tag_id:”bid_qr_001” as Unsafe
Problem of Reconnecting
Amit was unable to make Conductor App, so, it is being made by me, shubham
Conductor App is Crashing in a screen
Separate Database for storing Conductor’s Credentials created

## Slide 16: Meet 7 Jan
Learnt about Http Endpoints and MongoDB functions for database interaction
Created separate functions for GET, POST, PUT request in MongoDB
Created an app to insert new documents, read documents, and update certain keys in a document in MongoDB
Created functions in MongoDB for updating Asset status in documents
Created User app which is able to add a new entry ,scan Tag and generate Tagid , connect to MongoDB using Tagid and which gives an Alert whenever the Asset Status key is set to “Unsafe”
Conductor App is being created by amit

## Slide 17: Meet 24_Dec
Connected to MongoDB and updated database using Python Program
Learnt About Realm Service to connect to MongoDB Atlas
Created New Database, Collection and added documents in it from ESP32
Appended existing Database collections in MongoDB from ESP32

## Slide 18: Meet 17_Dec
1. Performed the experiment by covering the beacon with books
2. Performed the experiment by keeping the beacon inside luggage
3. Worst case connectivity range was found
4. Unsuccessful multiple attempts to connect to MongoDB using C program.
5. Unsuccessful attempts to connect to MongoDB from app
6. Learnt about Data API and User Access in MongoDB
7. Followed Tutorial of MongoDB C Driver from official website

## Slide 19: Meet 10_Dec
1.Performed the experiment putting the Beacon1 & Beacon2 inside the wooden box
2.Performed the experiment in open space with the Beacon1 & Beacon2
3. Worst case connectivity range

## Slide 20: Meet 19_Nov
Project Seminar ppt
MongoDB database Creation
MongoDB Compass(GUI And Shell)
MongoDB Atlas
ESP32 as i-Beacon
App for updating document in MongoDB (in progress)
ESP32 as client(in progress)

## Slide 21: ARCHITECTURE

## Slide 22
GATEWAY
USER’S APP
CONDUCTOR’S APP
CLOUD
Tags
ECU
MASTER
GATEWAY
CAN
BLE
Cellular Network
Cellular Network
Cellular Network
Cellular Network
Mobile phones of user and conductor
SMS
OBD
Lock Status
OTP,
Location Updates
Lock Status, Asset Status
OTP
Data to or from Database
Data to or from Database
GPS
UART
Location Coordinates

## Slide 23
ESP32
Power Supply
Gnd
Vin

## Slide 24
ESP32
Power Supply
Gnd
Vin
Servo motor
3.3V
G
G18

## Slide 25
ESP32
Power Supply
Gnd
Vin
Gnd
G16(Rx)
G17(Tx)
GSM Module
Tx
Rx
Gnd
GPS Module
Tx
Rx
Gnd
Vcc
3.3 V
G4
G2
Gnd

## Slide 26
 | BLE | WIFI | UWB
Location Accuracy | < 5 m* | < 10 m* | < 50 cm*
Range | Optimal: 0-25 m* Up to 100 m* | Optimal: 0-50 m* Up to 100 m* | Optimal: 0-50 m* Up to 200 m*
Latency | Typically, 3-5 s to get location* | Typically, 3-5 s to get location* | < 1 ms to get location*
Power Consumption | Low, option for coin cell battery in select hardware options | Moderate | Low, option for coin cell battery in select hardware options
Cost | low cost | high cost Low cost with existing Wi-Fi access points | high cost
Frequencies | 2.4 GHz | 2.4, 5 GHz | 3.1 – 10.6 GHz
Data Rate | Up to 2 Mbps | Up to 1 GBps | Up to 27 Mbps
Life time | More than 3 years | Less than 3 years | Less than 3 years
Availability in Mobile Phones | Yes | Yes | Only in Samsung note 20 ultra and i-phone 11 and newer version
Technology Comparison for Asset tracking

## Slide 27
There are various technologies available for Asset tracking such as WIFI, UWB, BLE etc. But we have selected BLE for our project because of its ultra-low power consumption (0.01 – 0.5 Watts) and availability of this technology in android phones.
There are several hardwares available such as HM-10, HM-19, ESP32 which support Bluetooth low energy and can work as BLE Beacons. Out of these ESP32 is chosen as it is lesser power consuming: 3V, 3 – 20 mA, Active(Tx): 120mA, Sleep: 10-150uA , and also it has a microcontroller in it which is helpful for connecting alarm. Also, it has a WIFI module which will be useful for communication with Cloud.
We have chosen MIT APP INVENTOR Platform for android app development as it is easy to use because of its GUI interface.
We have selected MongoDB as a database Platform because it is an open source platform and it is NoSQL based Platform. NoSQL databases provide a variety of benefits including flexible data models, horizontal scaling, lightning-fast queries, and ease of use for developers.
IMPORTANT POINTS

## Slide 28: Algorithm
App in user’s phone is used to scan QR code on the beacon tag getting attached to their asset. This adds an entry on the Cloud Platform and allows users to get continuous information of their asset’s location.
The beacons attached to the user’s assets will be sending BLE signals continuously.
The Gateway will receive signals from these Beacons. ESP32 as BLE Client with multiple Client Objects will act as Gateway. The ESP32 Bluetooth Low Energy supports up to 9 client devices for connection. We can use multiple Gateways and round robin technique to connect to all beacons.
  Round Robin Algorithm: For 96 beacons, We can use 3 Gateways each handling 32 Beacons per second in round robin of 8 Beacons per 250 ms.

## Slide 29
Calculation of Approximate distance: The received signal strength index of a signal is a value between 0 to 255 which indicates the strength of received signal. This value decreases with distance of travel. Distance travelled is given by the relation:
Distance = 10 ^ ((Measured Power -RSSI)/(10 * N)) where N is a value between 2 and 3 depending on environmental condition.
We get a RSSI of 80-100 for 5 meters distance.
There is an array which contains the last ten measured RSSI values. The approximate RSSI is calculated by taking an average of these ten values. This average value is used finally to decide whether our asset is in safe zone or not. When the calculated distance is more than 5 meters it sets the status flag in Cloud Platform as Unsafe, and an alarm is triggered to mobile phones of User and conductor as well as the alarm connected to beacons also starts to buzz.
Data in Cloud gets updated continuously from Gateway. There will be a status flag indicating Safe/Unsafe value depending on the calculated distance from Gateway.
App in conductor’s phone will be getting data directly from Gateway through Bluetooth communication. In case user have any problems like weak network, Low battery etc., this app can be used to perform actions like collect data of asset, disconnect beacon tag etc.

## Slide 30
Gateway
GSM Module
UART
TAG
BLE
LOCK
Cloud
Conductor APP
User APP
Cellular N/W
Cellular N/W
Cellular N/W

## Slide 31
OTP For Verification
APP
{Mob no}
Mongo DB
{Random OTP Generation }
Gateway
with GSM
SMS in User’s mobile number
OTP : xxxx
New Document in database
{
Mob : “xxx”
OTP : “xxx”
}
{Mob no, OTP}
{Mob no, OTP}
{OTP}
Mobile Data
Mobile Data
SMS
If both OTP match => verified

## Slide 32: Beacons
The job of these Beacons is to continuously emit BLE signals which will be received by the Gateway device.
These Beacons will be attached to our assets.
The received signal strength index of these signals will be used to calculate the approximate location of our asset.
GATEWAY
The job of the Gateway device is to capture BLE signals emitted by beacons and to calculate the approximate distance of asset from the Gateway.
This calculated distance will be updated to a cloud platform and also sent to an application software in the conductor’s mobile phone.

## Slide 33
Property | HM-10 | HM-19 | ESP32 | SEEK-IT
Power consumption | 2.5V~3.3VDC 50mA Active 8.5mA Sleep 50-200uA | 1.9 – 3.7V 50 mA Active 2.6mA Sleep 2.6mA | 3V 3 – 20 mA Active(Tx) 120mA Sleep 10-150uA | 3V 75mAh 0.5Watts
Bluetooth Technology | 4.0 | 5.0 | 4.0 | 5.0
Price | Rs 400-500 | Rs 730 | Rs 450-550 | Rs 765
Availability in india | Yes | No | Yes | Yes
Microcontroller Present | No | No | Yes | 
Hardware Comparison for Beacon and Gateway Selection

## Slide 34: Beacons:
ESP32 as BLE Server.
Features:
  2.4 GHz Wifi and Bluetooth Combo chip
  Supports BLE
  ROM: 448KB
  SRAM: 520KB
  FLASH: upto 16MB
  Supply: 2.2 – 3.6 V
  48 GPIO Pins
  Power Consumption : 3V, 3-20mA , Active State-120mA ,SleepState:-150uA
  Bluetooth Technology 4.0

## Slide 35: Gateway:
ESP32 as BLE Client with multiple Client Objects.
The ESP32 Bluetooth LE supports up to 9 client devices for connection. It is recommended to hold this number within 3.(Same limitation for Raspberry pi as Gateway)
(https://docs.espressif.com/projects/espressif-esp-faq/en/latest/software-framework/ble-bt.html {Point 34} )
We can use multiple Gateways and round robin technique to connect to all beacons.
  For 96 beacons, We can use 3 Gateways each handling 32 Beacons per second in round robin of 8 Beacons per 250 ms.

## Slide 36
https://lastminuteengineers.com/sim900-gsm-shield-arduino-tutorial/
GSM Module

## Slide 37
Serial Terminal
Antenna
Power Suppy
(Tx,Rx,Gnd)
Microphone terminals
Speaker terminals
Power Button
(Hold Press)
Reset Button
N/W Status
Ring Status
{
Led Indicators

## Slide 38
We can use this shield to accomplish almost anything a normal cell phone can; SMS text messages, Make or receive phone calls, connecting to internet through GPRS, TCP/IP, and more! To top it off, the shield supports quad-band GSM/GPRS network, meaning it works pretty much anywhere in the world.
Sim card Holder
GSM MODULE

## Slide 39
The SIM900 shield packs a surprising amount of features into its little frame. Some of them are listed below:
Supports Quad-band: GSM850, EGSM900, DCS1800 and PCS1900
Connect onto any global GSM network with any 2G SIM
Make and receive voice calls using an external earphone & electret microphone
Send and receive SMS messages
Send and receive GPRS data (TCP/IP, HTTP, etc.)
Scan and receive FM radio broadcasts
Transmit Power:
  Class 4 (2W) for GSM850
  Class 1 (1W) for DCS1800
Serial-based AT Command Set
U.FL and SMA connectors for cell antenna
Accepts Full-size SIM Card
PWR: This LED is connected to the shield’s power supply line. If this LED is on, the shield is receiving power.
Status: This LED indicates SIM900’s working status. If this LED is on, the chip is in working mode.
Netlight: This LED indicates the status of your cellular network. It’ll blink at various rates to show what state it’s in.
off: The SIM900 chip is not running
64ms on, 800ms off: The SIM900 chip is running but not registered to the cellular network yet.
64ms on, 3 seconds off: The SIM900 chip is registered to the cellular network & can send/receive voice and SMS.
64ms on, 300ms off: The GPRS data connection you requested is active.
LED STATUS INDICATORS

## Slide 41
Arduino Code – Testing AT Commands

## Slide 42
Arduino Code – Sending SMS
Arduino Code – Reading SMS

## Slide 43
Arduino Code – Making Call
Arduino Code – Receiving Call

## Slide 44
Expanding Arduino SoftwareSerial Buffer Size
If your message is long enough just like ours, then you’ll probably receive it with some missing characters. This is not because of a faulty code. Your SoftwareSerial receive buffer is getting filled up and discarding characters. You are not reading fast enough from the buffer.
The simplest solution to this is to increase the size of the SoftwareSerial buffer from its default size of 64 bytes to 256 bytes (or smaller, depending on what works for you).
On a Windows PC, go to C:\Users\user\Documents\Arduino\libraries\EspSoftwareSerial-6.16.1\src
Open Softwareserial.h

## Slide 46
A hardware serial, as the name suggests, denotes that a dedicated piece of hardware (UART) enables Serial communication. In Arduino Uno, for instance, pins 0 and 1 have UART support,and they are connected to the USB via a USB-to-UART converter. That facilitates communication between your computer/laptop and the Arduino. While Arduino Uno has a single Hardware Serial, other boards like Mega have multiple. They are accessed using Serial, Serial1, Serial2, and so on.
Software serial is a library that replicates the hardware serial behavior on other digital pins of the Arduino, using (you guessed it) software. You can have more than one software serials running in parallel, with the limitation being that only one can receive data at a time.
https://www.tutorialspoint.com/difference-between-hardware-serial-and-software-serial-in-arduino
When you need multiple serial devices to be connected, it is possible to create multiple software serial ports. But due to hardware limitation, Arduino UNO can only listen to one software serial at a time.

## Slide 47
The ESP32 has 3 different Serial Ports (UART). You can just use one of them:
Serial0: RX0 on GPIO3, TX0 on GPIO1 Serial1: RX1 on GPIO9(SD2), TX1 on GPIO10(SD3) (+CTS1 and RTS1) Serial2: RX2 on GPIO16, TX2 on GPIO17 (+CTS2 and RTS2)
We use Serial2.begin(19200, SERIAL_8N1,16,17);//baud,protocol,rx,tx
/* * There are three serial ports on the ESP known as U0UXD, U1UXD and U2UXD.
U0UXD is used to communicate with the ESP32 for programming and during reset/boot.
* U1UXD is unused and can be used for your projects. Some boards use this port for SPI Flash access though
* U2UXD is unused and can be used for your projects. * */
https://circuits4you.com/2018/12/31/esp32-hardware-serial2-example/

## Slide 49: GPS Module
https://create.arduino.cc/projecthub/ruchir1674/how-to-interface-gps-module-neo-6m-with-arduino-8f90ad
https://www.electronicwings.com/arduino/gps-module-interfacing-with-arduino-uno

## Slide 50
In approximate order this would be my summary of the reasons behind a GPS that 'does not work'
GPS is indoors
GPS is connected incorrectly
Arduino program uses the wrong GPS baud rate
Arduino program is not correct
GPS is faulty
Arduino is faulty

## Slide 51
What is GPS?
The Global Positioning System (GPS) is a satellite-based navigation system made up of at least 24 satellites. GPS works in any weather conditions, anywhere in the world, 24 hours a day, with no subscription fees or setup charges.
How GPS works?
GPS satellites circle the Earth twice a day in a precise orbit. Each satellite transmits a unique signal and orbital parameters that allow GPS devices to decode and compute the precise location of the satellite. GPS receivers use this information and trilateration to calculate a user's exact location. Essentially, the GPS receiver measures the distance to each satellite by the amount of time it takes to receive a transmitted signal. With distance measurements from a few more satellites, the receiver can determine a user's position and display it.
To calculate your 2-D position (latitude and longitude) and track movement, a GPS receiver must be locked on to the signal of at least 3 satellites. With 4 or more satellites in view, the receiver can determine your 3-D position (latitude, longitude and altitude). Generally, a GPS receiver will track 8 or more satellites, but that depends on the time of day and where you are on the earth.
Once your position has been determined, the GPS unit can calculate other information, such as:
Speed, Bearing, Track, Trip dist, Distance to destination
What's the signal?
GPS satellites transmit at least 2 low-power radio signals. The signals travel by line of sight, meaning they will pass through clouds, glass and plastic but will not go through most solid objects, such as buildings and mountains. However, modern receivers are more sensitive and can usually track through houses.
A GPS signal contains 3 different types of information:
Pseudorandom code is an I.D. code that identifies which satellite is transmitting information. You can see which satellites you are getting signals from on your device's satellite page.
Ephemeris data is needed to determine a satellite's position and gives important information about the health of a satellite, current date and time.
Almanac data tells the GPS receiver where each GPS satellite should be at any time throughout the day and shows the orbital information for that satellite and every other satellite in the system.

## Slide 52: Detailed working of GPS Module
Global Positioning System (GPS) is a satellite-based system that uses satellites and ground stations to measure and compute its position on Earth.
GPS is also known as Navigation System with Time and Ranging (NAVSTAR) GPS.
GPS receiver needs to receive data from at least 4 satellites for accuracy purpose. GPS receiver does not transmit any information to the satellites.
These GPS satellites transmit information signal over radio frequency (1.1 to 1.5 GHz) to the receiver. With the help of this received information, a ground station or GPS module can compute its position and time.
How GPS Works?

## Slide 53
How GPS Receiver Calculates its Position and Time
GPS receiver receives information signals from GPS satellites and calculates its distance from satellites. This is done by measuring the time required for the signal to travel from satellite to the receiver.
Distance = Speed * Time
Where,
Speed = Speed of Radio signal which is approximately equal to the speed of light i.e. 3 * 108 ms-1
Time = Time required for a signal to travel from the satellite to the receiver.
By subtracting the sent time from the received time, we can determine the travel time.

## Slide 54
To determine distance, both the satellite and GPS receiver generate the same pseudocode signal at the same time.
The satellite transmits the pseudocode; which is received by the GPS receiver.
These two signals are compared and the difference between the signals is the travel time.
Now, if the receiver knows the distance from 3 or more satellites and their location (which is sent by the satellites), then it can calculate its location by using Trilateration method.
GPS receiver module gives output in standard (National Marine Electronics Association) NMEA string format. It provides output serially on Tx pin with default 9600 Baud rate.
This NMEA string output from GPS receiver contains different parameters separated by commas like longitude, latitude, altitude, time etc. Each string starts with ‘$’ and ends with carriage return/line feed sequence.
E.g.
$GPGGA,184237.000,1829.9639,N,07347.6174,E,1,05,2.1,607.1,M,-64.7,M,,0000*7D
$GPGSA,A,3,15,25,18,26,12,,,,,,,,5.3,2.1,4.8*36

## Slide 56
NEO-6M GPS Chip
The heart of the module is a NEO-6M GPS chip from u-blox. It can track up to 22 satellites on 50 channels and achieves the industry’s highest level of sensitivity i.e. -161 dB tracking, while consuming only 45mA supply current. The u-blox 6 positioning engine also boasts a Time-To-First-Fix (TTFF) of under 1 second. One of the best features the chip provides is Power Save Mode(PSM). It allows a reduction in system power consumption by selectively switching parts of the receiver ON and OFF. This dramatically reduces power consumption of the module to just 11NEO-6M GPS Chip
The heart of the module is a NEO-6M GPS chip from u-blox. It can track up to 22 satellites on 50 channels and achieves the industry’s highest level of sensitivity i.e. -161 dB tracking, while consuming only 45mA supply current. The u-blox 6 positioning engine also boasts a Time-To-First-Fix (TTFF) of under 1 second. One of the best features the chip provides is Power Save Mode(PSM). It allows a reduction in system power consumption by selectively switching parts of the receiver ON and OFF. This dramatically reduces power consumption of the module to just 11mA making it suitable for power sensitive applications like GPS wristwatch. The necessary data pins of NEO-6M GPS chip are broken out to a "0.1″ pitch headers. This includes pins required for communication with a microcontroller over UART.
Note:- The module supports baud rate from 4800bps to 230400bps with default baud of 9600.
mA making it suitable for power sensitive applications like GPS wristwatch. The necessary data pins of NEO-6M GPS chip are broken out to a "0.1″ pitch headers. This includes pins required for communication with a microcontroller over UART.
Note:- The module supports baud rate from 4800bps to 230400bps with default baud of 9600.

## Slide 57
No Blinking ==> means It is searching for satellites
Blink every 1s – means Position Fix is found
Position Fix LED Indicator
3.3V LDO Regulator
The operating voltage of the NEO-6M chip is from 2.7 to 3.6V. But, the module comes with MIC5205 ultra-low dropout 3V3 regulator from MICREL. The logic pins are also 5-volt tolerant, so we can easily connect it to an Arduino or any 5V logic microcontroller without using any logic level converter.

## Slide 58
Battery & EEPROM
The module is equipped with an HK24C32 two wire serial EEPROM. It is 4KB in size and connected to the NEO-6M chip via I2C.The module also contains a rechargeable button battery which acts as a super-capacitor.
An EEPROM together with battery helps retain the battery backed RAM (BBR). The BBR contains clock data, latest position data (GNSS or bit data) and module configuration. But it is not meant for permanent data storage.
As the battery retains clock and last position, time to first fix (TTFF) significantly reduces to 1s. This allows much faster position locks.
Without the battery the GPS always cold-start so the initial GPS lock takes more time. The battery is automatically charged when power is applied and maintains data for up to two weeks without power.

## Slide 59
Arduino Tx(3) Gps Rx
Arduino Rx(4) Gps Tx
Arduino 5V Gps Vcc
Arduino GND Gps GND

## Slide 61
CODE: (Arduino_GPS3 working in IDE)
https://www.electronicwings.com/arduino/gps-module-interfacing-with-arduino-uno

## Slide 63
Longitude
The demarcation of the longitude coordinate is done with lines going up and down are called the meridians. A figure to the right shows a few meridians. Longitude ranges from 0° to 180° East and 0° to 180° West. The longitude angle is measured from the center of the earth as shown in the earth graphic to the right.
The zero point of longitude is defined as a point in Greenwich, England called the Prime Meridian. (Why Greenwich of all places?) 180° away from the Prime Meridian is the line called the International Date Line. Unlike the Prime Meridian, the International Date line isn't straight for political/social reasons.
Latitude
The demarcation of the latitude coordinate is done with circles on the globe parallel to the equator. These parallel circles, fittingly enough, are called parallels of latitude. The figure to the right shows several parallels of latitude. Latitude goes for 0° at the equator to +90° N at the North Pole or -90° S at the South Pole where the angle is also measured from the center of the earth as shown in the earth graphic to the right.
The primary unit in which longitude and latitude are given is degrees (°). There are 360° of longitude (180° E ↔ 180° W) and 180° of latitude (90° N ↔ 90° S). Each degree can be broken into 60 minutes (’). Each minute can be divided into 60 seconds (”). For finer accuracy, fractions of seconds given by a decimal point are used. A base-sixty notation is called a sexagesimal notation.
Units of Longitude and Latitude

## Slide 64
Example: Convert decimal degrees 156.742 to degrees minutes seconds
The whole number is degrees. So 156.742 gives you 156 degrees.
Multiply the remaining decimal by 60. 0.742*60 = 44.52, so the whole number 44 equals minutes.
Multiply the remaining decimal by 60. 0.52*60 = 31.2, so the whole number 31 equals seconds.
Decimal degrees 156.742 converts to 156 degrees, 44 minutes and 31 seconds, or 156° 44' 31".
What is DMS?
DMS is the abbreviation for Degrees Minutes Seconds. Degrees minutes seconds (DMS) are special type of units used for measuring angles, as an alternative to decimal way to stating the size of an angle. It is a known fact that there are 360 degrees in a whole circle, with 1/60th of those being 1 minute, and 1/60th of one minute being 1 second. DMS includes degrees (°), minutes ('), seconds (''), with the corresponding symbols, and a size of any angle can be stated like, for example, 30 degrees, 10 minutes, 50 seconds.

## Slide 65
Experiment 6 and 7 added in Experiment Section

## Slide 66
Converting G-map Route to array of Co-ordinates(gpx{GPS exchange} file)

## Slide 67
https://gpx.cgtk.co.uk/v2/CsGF6 (Convert a route in location co-ordinates)

## Slide 68
Converting a gpx to Gmap Route

## Slide 69
Open : https://mymaps.google.com/
Click on Create new map ->Add layer then import
Sometimes after clicking Creatre new map, it gets created but nothing appears in screen. We have to revisit the site and then click on Untitled map and open it. Also Sometimes it doesn’t open in my laptop, so I have to use incognito mode to open this website.

## Slide 70
ON ZOOMING

## Slide 71
Converting CSV file to G-Map Route

## Slide 72
For gpx – csv converter use this:
https://mygeodata.cloud/converter/gpx-to-csv
Open : https://mymaps.google.com/
Click on Create new map ->Add layer then import
Sometimes after clicking Creatre new map, it gets created but nothing appears in screen. We have to revisit the site and then click on Untitled map and open it. Also Sometimes it doesn’t open in my laptop, so I have to use incognito mode to open this website.

## Slide 73
IISC to COORG Gmap-Route as an array of locations from csv file

## Slide 74
Each Lattitude, Longitude plot

## Slide 75: EXPERIMENT 1

## Slide 76: Esp32 as i-Beacon EXPERIMENT 1
Components used: 1.)ESP32 2.)BLE Scanner app
Experiment was performed in ES1-lab
Esp32 was working as ble i-Beacon and signals were scanned by android app.
Code used is attached in the “code” section of PPT
Esp32 was powered through laptop and different measurement was taken by varying distance between mobile and Esp32
Results were noted

## Slide 77
S.NO. | ACTUAL DISTANCE | MEASURED DISTANCE
1 | 14 cm | 12 - 16 cm
2 | 30 cm | 28 - 41 cm
3 | 1 m | 1 - 1.4 m
4 | 3.5 m | 3.8 – 4.2 m
5 | 5m | 5.01 - 6.31 m
RESULTS:

## Slide 80: EXPERIMENT 2

## Slide 81: Experiment 2- Esp32 as beacon in different position
Different positions | Actual distance | Measured distance
up | 1 meter | 0.89 – 1.41 m
left | 1 meter | 0.81 – 1.26 m
down | 1 meter | 0.63 – 1.10 m
right | 1 meter | 0.35 – 0.87 m

## Slide 82
Different positions | Actual distance | Measured distance
 | 5 meter | 3.46 – 4.47 m
 | 5 meter | 3.18 – 4.21 m
 | 5 meter | 3.15 – 4.30 m
 | 5 meter | 3.51 – 4.58 m

## Slide 83: EXPERIMENT 3

## Slide 84: Experiment-3 Putting the Beacon inside the bag
Sr. No | Actual distance | Measured distance
1 | 3 meter | 1.26 – 2.10 meter
2 | 5 meter | 3.15 – 4.21 meter

## Slide 85: ARRANGEMENT

## Slide 86
3 wooden drawer are present in ES2 lab
Beacons are kept in bottom drawer
Items present in drawer:
  3 computer mouses are present
  2 data cables are present
  2 Power supplier and Paper packets are present

## Slide 87
Measured distance Actual Distance | M1(meter) | M2(meter) | M3(meter) | M4(meter) | M5(meter | Average
1 meter | 1.58 | 1.41 | 2.00 | 1.78 | 1.26 | 1.606
2 meter | 2.24 | 2.51 | 2.82 | 2.00 | 3.16 | 2.546
3 meter | 2.51 | 3.16 | 2.82 | 3.98 | 3.55 | 3.204
4 meter | 2.58 | 3.41 | 3.12 | 3.58 | 4.00 | 3.338
6 meter | 5.62 | 4.47 | 5.01 | 6.31 | 8.91 | 6.064
1.Performed the experiment putting the Beacon1 inside the wooden box

## Slide 88
Measured distance Actual Distance | M1(meter) | M2(meter) | M3(meter) | M4(meter) | M5(meter) | Average
1 meter | 1.00 | 0.79 | 1.58 | 1.12 | 1.26 | 1.15
2 meter | 2.51 | 2.24 | 2.00 | 1.78 | 2.51 | 2.208
3 meter | 2.00 | 2.24 | 2.51 | 2.82 | 2.24 | 2.362
4 meter | 3.98 | 3.55 | 2.82 | 3.16 | 4.47 | 3.596
6 meter | 7.94 | 10 | 8.91 | 7.08 | 7.94 | 8.374
2.Performed experiment putting the Beacon2 inside the wooden box

## Slide 89: Worst case range
14 meters
Beacons get disconnected from the BLE APP as we move distance above 14 meters

## Slide 90
Measured distance Actual Distance | M1(meter) | M2(meter) | M3(meter) | M4(meter) | M5(meter | Average
1 meter | 1.12 | 1.24 | 1.6 | 1.4 | 1.12 | 1.296
2 meter | 2.2 | 2.31 | 2.51 | 2.65 | 3.11 | 2.556
3 meter | 2.61 | 2.89 | 3.18 | 3.55 | 3.81 | 3.208
4 meter | 2.89 | 3.44 | 3.15 | 4.12 | 4.38 | 3.596
6 meter | 5.38 | 4.98 | 5.38 | 7.05 | 7.89 | 6.136
3.Performed the experiment in open space with the Beacon1

## Slide 91
Measured distance Actual Distance | M1(meter) | M2(meter) | M3(meter) | M4(meter) | M5(meter) | Average
1 meter | 1.18 | 1.31 | 1.26 | 1.58 | 1.6 | 1.386
2 meter | 2.55 | 2.21 | 2.4 | 1.89 | 2.51 | 2.312
3 meter | 2.89 | 3.21 | 3.4 | 2.89 | 3.18 | 3.114
4 meter | 3.89 | 4.02 | 3.89 | 3.76 | 4.38 | 3.988
6 meter | 7.02 | 8.12 | 8.38 | 7.18 | 7.89 | 7.718
4.Performed the experiment in open space with the Beacon2

## Slide 92: EXPERIMENT 4

## Slide 93: ARRANGEMENT 1 (Beacon inside the heap of books)

## Slide 94: ARRANGEMENT 2 (Beacon inside the luggage)

## Slide 95
Performed the experiment putting beacon inside the heap of books
Measured distance Actual distance | M1 (meter) | M2 (meter) | M3 (meter) | M4 (meter) | M5 (meter) | Average
1 meter | 0.63 | 0.85 | 0.45 | 0.56 | 0.71 | 0.628
2 meter | 0.79 | 0.85 | 1.00 | 0.71 | 0.79 | 0.828
3 meter | 1.26 | 1.41 | 1.5 | 1.63 | 1.41 | 1.442
4 meter | 1.79 | 2.13 | 2.26 | 1.91 | 2.21 | 2.06

## Slide 96: Performed the experiment putting beacon inside the luggage
Measured distance Actual distance | M1 (meter) | M2 (meter) | M3 (meter) | M4 (meter) | M5 (meter) | Average
1 meter | 0.45 | 0.53 | 0.49 | 0.67 | 0.56 | 0.54
2 meter | 1.21 | 0.97 | 1.41 | 1.12 | 1.54 | 1.25
3 meter | 1.79 | 2.01 | 2.33 | 1.93 | 2.12 | 2.036
4 meter | 2.31 | 2.53 | 2.79 | 2.45 | 2.81 | 2.578

## Slide 97: Worst case range
5 meters
Beacons get disconnected from the BLE APP as we move distance above 5 meters

## Slide 98: Comparison between firebase and mongoDB
Common comparison | Firebase | MongoDB
Release year | 2012 | 2009
Developed by | Google | MongoDB
performance | Performance rate less than MongoDB | Despite of high traffics the apps perform seamlessly
Supported language | Java, C, C++, PHP | Java, C, Perl, Python, PHP
Querying limit | The querying capabilities of firebase is limited | The querying capabilities of mongoDB is not limited
Security | Less secure in comparison to mongoDB | More secure in comparison to Firebase
applications | Good for small-scale mobile applications | Best for large-scale mobile applications

## Slide 99: Security
MongoDB Atlas offers built-in security controls for all your data. Enable enterprise-grade features to integrate with your existing security protocols and compliance standards.
With MongoDB Atlas, your data is protected with preconfigured security features for authentication, authorization, encryption, and more

## Slide 100
Network Isolation MongoDB Atlas dedicated clusters are deployed in a unique Virtual Private Cloud (VPC) with dedicated firewalls. Access must be granted by an IP access list or VPC Peering.
Role-based access management
Configure sophisticated role-based access rules to control which users and teams can access, manipulate, and delete data in your databases
End-to-end encryption
All network traffic is encrypted using Transport layer Security (TLS), with flexibility to configure the minimum TLS protocol version. Encryption for data at rest is automated using encrypted storage volumes.
Enable automatic client-side field level encryption to encrypt sensitive data before it leaves the application and lands in the cloud.

## Slide 101: EXPERIMENT 5 : CAN Bus communication between two ESP32

## Slide 102
ESP32 (1)
5V GND G5 G4
V G Tx Rx
CAN (1)
ESP32 (2)
5V GND G5 G4
V G Tx Rx
CAN (2)
BLOCK DIAGRAM
120 Ω
120 Ω

## Slide 103
In this experiment we are trying to communicate between two ESP32 using CAN Bus:
First ESP32 module: Receiving string, Converting to upper case and Respond back
Second ESP32 module: Sending the string that need to be converted to upper case, Receiving response and show it to Terminal

## Slide 104
Terminal resistors are needed in CAN bus systems because CAN communication flows are two-way. The termination at each end absorbs the CAN signal energy, ensuring that this is not reflected from the cable ends. Such reflections would cause interference and potentially damaged signals.
The reflection challenge grows with the length of the cables as well as the CAN bus bit rate. This is why it is critical to add proper termination in larger CAN networks.
For best results, the CAN bus termination should match the nominal impedance of the cables, which for ISO 11898-2 (high speed CAN) is specified at 120 Ohm. Hence 120 Ohm termination adaptors are considered the standard for CAN bus.

## Slide 105
OUTPUT

## Slide 106: Experiment 6 Gps Module testing with Arduino

## Slide 110: Experiment 7: GPS module merged with GSM

## Slide 112
Location Tracked by GPS

## Slide 113: Advanced Encryption Standard

## Slide 114
Not https therefore encryption needed

## Slide 115
SUBSTITUTION WORD
SHIFT ROWS
MIX COLUMNS
Message(128 bits)
ADDING ROUND KEYS

## Slide 119
AddRoundKey() Transformation
In the AddRoundKey() transformation, a Round Key is added to the State by a simple bitwise
XOR operation.

## Slide 120
Affine Transformantion : A transformation consisting of multiplication by a matrix followed by transformation the addition of a vector.
Cipher Series of transformations that converts plaintext to ciphertext using the Cipher Key.
Cipher Key Secret, cryptographic key that is used by the Key Expansion routine to generate a set of Round Keys; can be pictured as a rectangular array of bytes, having four rows and Nk columns.
Ciphertext Data output from the Cipher or input to the Inverse Cipher.
Inverse Cipher Series of transformations that converts ciphertext to plaintext using the Cipher Key.
Key Expansion Routine used to generate a series of Round Keys from the Cipher Key
Plaintext Data input to the Cipher or output from the Inverse Cipher.
Rijndael Cryptographic algorithm specified in this Advanced Encryption Standard (AES).
Round Key Round keys are values derived from the Cipher Key using the Key Expansion routine; they are applied to the State in the Cipher and Inverse Cipher.
State Intermediate Cipher result that can be pictured as a rectangular array of bytes, having four rows and Nb columns.
S-box Non-linear substitution table used in several byte substitution transformations and in the Key Expansion routine to perform a one-for-one substitution of a byte value

## Slide 121
For the AES algorithm, the length of the input block, the output block and the State is 128 bits.

## Slide 122
Encryption
Symmetric Encryption
Asymmetric Encryption
Single Passphrase for encryption and decryption
Separate Keys : Public and private
Public is for encryption and Private is for Decryption. Anyone with Public key can Encrypt the data before sending. Only the authorised person can decrypt the data with private key.
Although the public and private keys are mathematically related, private keys can’t be derived by knowing the public key.
Used in https

## Slide 123
We have used Assymetric algorithm for encryption of our Database.
Asymmetric algorithms¶
Asymmetric cryptography is a branch of cryptography where a secret key can be divided into two parts, a public key and a private key . The public key can be given to anyone, trusted or not, while the private key must be kept secret (just like the key in symmetric cryptography).
Encryption with asymmetric cryptography works in a slightly different way from symmetric encryption. Someone with the public key is able to encrypt a message, providing confidentiality, and then only the person in possession of the private key is able to decrypt it

## Slide 124
We are using Key length of 1024 which can encrypt string of at max length 128.(Key length>= 8*String length)
If we use higher Key length then Encryption time increases and if we use lesser length then max string length decreases.
We have Generated our public key(For Encryption) and Private key(For Decryption) from online Key pair Generator. But we have learnt how to generate key pairs:
      online RSA encryption public - private key pair generator:
        https://www.devglan.com/online-tools/rsa-encryption-decryption
RSA Encryption relies on Factors and large prime numbers
    Ex:
    Factors of 1147 are 31 and 37
    Factors of 8,616,460,799 are 89681 and 96079 (prime numbers)
    Factors of 1,081,881,451,307,197,929,383 are beyond the reach of computer calculation

## Slide 125
Two hundred digit prime number when multiplied, gives this two hundred digit number.
CPU time to find factors : 75 years for a single 2.2GHz operation based computer.

## Slide 126
RSA Algorithm
Key Generation:
  Choose two very large prime numbers p and q.
  N=p*q
  Euler totient T=(1-p)(1-q)
  Choose e and d such that : (e*d) MOD T = 1
  PUBLIC KEY : (N,e)
  PRIVATE KEY: (N,d)
2. Encryption : (Msg)e MOD N = Encrypted msg
3. Decryption : (Encrypted Msg)d MOD N = Original msg

## Slide 127
Ex:
p = 2 ,q = 7
N = 14
T = 1*6 = 6
Let e=5 , d=11 { 55 % 6 = 1}
Public key(5,14)
Private key(11,14)
Message : “B”  ASCII = 66 but for simplicity lets take A=1,B=2,C=3,D=4
Encryption(Key: 5,14 Msg: 2): (2)5 MOD 14 = 4 ”D”
Decryption(Key:11,14 Msg:4): (4)11 MOD 14 = 2 ”B”

## Slide 128
TYPE 1 (only password encrypted. If we want monitoring in MongoDB then it is still possible)
TYPE 3(Everything encrypted. If we want monitoring in MongoDB then it is not possible)
TYPE 2
(Emp_id left so that at the time of login we don’t need to encrypt again and also successful entry can be verified)
Encrypted Database

## Slide 130: CLOUD:
MongoDB will be used as Cloud Database which will store information of all beacon’s location.
MongoDB stores data in flexible, JSON(“key”: “value”)-like documents, meaning fields can vary from document to document and data structure can be changed over time. Whereas in SQL database information is stored in form of tables.
The document model maps to the objects in our application code, making data easy to work with
Provide powerful ways to access and analyze our data
MongoDB is free to use.

## Slide 131: MongoDB
There are 2 ways of database creation:
SHELL : Shell commands
2.MongoDB Compass : GUI
Each database have some collections.
Each collection have some documents in it.

## Slide 132: MongoDB Shell Basic Commands
show dbs // to display available databases
        It will not show the database with no collection.
use database_name //if exist then opens that database otherwise creates a new database with that name
db // shows current database in which we are
show collections // show available collection in current database
db.collection_name.find() // show data inside collection we will get first or top 20 data
db.collection_name.find().pretty() // show data inside collection
db.createCollection(“collection_name”) // ok response on collection creation
db.collection_name.insert({“name”: “shubham” ,”age” : “23”, “country” : “India”})
Db.collection_name.insertMany([{“name”: “shubham” ,”age” : “23”, “country” : “India”},{“name”: “saurav” ,”age” : “13”}])

## Slide 133: First Database Creation
mydatabase1->Travellor_data->
(database) (collection)
use mydatabase1
db.createCollection("Travellor_data")
db.Travellor_data.insertMany([{"Uid":"U01","Bid":"001","Source":"Ranchi","Destination":"Bangalore","Asset_Status":"Safe"}])
db.Travellor_data.insertMany([{"Uid":"U02","Bid":"002","Source":"Ranchi","Destination":"Bangalore","Asset_Status":"Safe"}])
db.Travellor_data.find().pretty()

## Slide 134: MongoDB Atlas(Cloud)
Steps :
  Create a cluster in https://cloud.mongodb.com
  Create a project in that cluster
  Connect -> connect with MongoDB compass -> copy URL -> use that URL in MongoDB compass to connect
  “mongodb+srv://shubham:<password>@cluster0.zqakj.mongodb.net/test”
  Connect -> connect your application to your cluster using MongoDB’s native driver-> copy connection string -> use that string to connect through app
  “mongodb+srv://shubham:<password>@cluster0.zqakj.mongodb.net/myFirstDatabase?retryWrites=true&w=majority”

## Slide 135: MongoDB Atlas

## Slide 136
URL Endpoint: https://data.mongodb-api.com/app/data-qghaw/endpoint/data/beta
Data Api-id: GulxASKRrONWiS5xi0s2gQTCos0euFEklmv9EdlUgCa8kwKMdIyHiE4OSel77Yc3

## Slide 137
Organization-API:
Public(username): qxekrsvu
Private(Password): fec45dfd-b45d-4af4-a031-a9a99571d67f

## Slide 138
STEPS FOR GIVING ACCESS TO CLUSTER:
https://www.youtube.com/watch?v=esKNjzDZItQ
Create a cluster
Network access  Add IP  Visible to all
Database Access  Add a new Database user(shubham, Shubham100)  Permission(Atlas Admin) create

## Slide 139: STEPS FOR INSTALLING MONGODB C DRIVER http://mongoc.org/libmongoc/current/installing.html#prerequisites-for-libmongoc

## Slide 140
Installing libraries for MongoDB C Driver:
Install libmongoc with a Package Manager:
$ apt-get install libmongoc-1.0-0
Install libbson with a Package Manager:
$ apt-get install libbson-1.0-0
Build environment
Prerequisites for libmongoc:OpenSSL is required for authentication or for TLS connections to MongoDB. Kerberos or LDAP support requires Cyrus SASL.
$ sudo apt-get install cmake libssl-dev libsasl2-dev
Prerequisites for libbson: The only prerequisite for building libbson is cmake. The command lines above can be adjusted to install only cmake.
$ brew install cmake
Configuring the build
The following snippet will download and extract the driver, and configure it:
$ wget https://github.com/mongodb/mongo-c-driver/releases/download/1.20.0/mongo-c-driver-1.20.0.tar.gz
$ tar xzf mongo-c-driver-1.20.0.tar.gz
$ cd mongo-c-driver-1.20.0
$ mkdir cmake-build
$ cd cmake-build
$ cmake -DENABLE_AUTOMATIC_INIT_AND_CLEANUP=OFF ..

## Slide 141
The -DENABLE_AUTOMATIC_INIT_AND_CLEANUP=OFF option is recommended, see Initialization and cleanup. Another useful cmake option is -DCMAKE_BUILD_TYPE=Release for a release optimized build and -DCMAKE_BUILD_TYPE=Debug for a debug build. For a list of all configure options, run cmake -L ...
If cmake completed successfully, you will see a considerable amount of output describing your build configuration. The final line of output should look something like this:
-- Build files have been written to: /home/user/mongo-c-driver-1.20.0/cmake-build
If cmake concludes with anything different, then it is likely an error occurred.
mongo-c-driver contains a copy of libbson, in case your system does not already have libbson installed. The configuration will detect if libbson is not installed and use the bundled libbson.
Additionally, it is possible to build only libbson by setting the -DENABLE_MONGOC=OFF option:
$ cmake -DENABLE_AUTOMATIC_INIT_AND_CLEANUP=OFF -DENABLE_MONGOC=OFF ..

## Slide 142
Preparing a build from a git repository clone
$ git clone https://github.com/mongodb/mongo-c-driver.git
$ cd mongo-c-driver
$ git checkout 1.20.0 # To build a particular release
$ python build/calc_release_version.py > VERSION_CURRENT
$ mkdir cmake-build
$ cd cmake-build
$ cmake -DENABLE_AUTOMATIC_INIT_AND_CLEANUP=OFF ..
Executing a build¶
Building on Unix, macOS, and Windows (MinGW-W64 and MSYS2)
$ cmake --build .
$ sudo cmake --build . --target install
The following command can be used (for Ninja and Makefile-based build systems) to list all available targets:
$ cmake --build . Help

## Slide 143
Generating the documentation
Install Sphinx, then:
$ cmake -DENABLE_MAN_PAGES=ON -DENABLE_HTML_DOCS=ON ..
$ cmake --build . --target mongoc-doc
To build only the libbson documentation:
$ cmake -DENABLE_MAN_PAGES=ON -DENABLE_HTML_DOCS=ON ..
$ cmake --build . --target bson-doc
The -DENABLE_MAN_PAGES=ON and -DENABLE_HTML_DOCS=ON can also be added as options to a normal build from a release tarball or from git so that the documentation is built at the same time as other components.
Uninstalling the installed components
There are two ways to uninstall the components that have been installed. The first is to invoke the uninstall program directly. On Linux/Unix:
$ sudo /usr/local/share/mongo-c-driver/uninstall.sh
Additional Options for Integrators
In the event that you are building the BSON library and/or the C driver to embed with other components and you wish to avoid the potential for collision with components installed from a standard build or from a distribution package manager, you can make use of the BSON_OUTPUT_BASENAME and MONGOC_OUTPUT_BASENAME options to cmake.
$ cmake -DBSON_OUTPUT_BASENAME=custom_bson -DMONGOC_OUTPUT_BASENAME=custom_mongoc ..
XXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXX

## Slide 144
TUTORIAL : http://mongoc.org/libmongoc/current/tutorial.html
Starting MongoDB
$ mongo --host localhost --port 27017
MongoDB shell version: 3.0.6
connecting to: localhost:27017/test
>
pkg-config¶
use pkg-config on the command line to set header and library paths:
gcc -o hello_mongoc hello_mongoc.c $(pkg-config --libs --cflags libmongoc-1.0)
Or to statically link to libmongoc:
gcc -o hello_mongoc hello_mongoc.c $(pkg-config --libs --cflags libmongoc-static-1.0)
Specifying header and include paths manually
If you aren’t using CMake or pkg-config, paths and libraries can be managed manually.
$ gcc -o hello_mongoc hello_mongoc.c \
-I/usr/local/include/libbson-1.0 -I/usr/local/include/libmongoc-1.0 \
-lmongoc-1.0 -lbson-1.0
$ ./hello_mongoc
{ "ok" : 1.000000 }

## Slide 145
Atlas Connection String : mongodb+srv://shubham:Shubham100@cluster0.zqakj.mongodb.net/ASSET_INFO?retryWrites=true&w=majority
References:
https://cloud.mongodb.com/v2/6184fca65f4a4211fc9366a6#clusters
https://docs.mongodb.com/drivers/c/
http://mongoc.org/libmongoc/current/installing.html
http://mongoc.org/libmongoc/current/tutorial.html
http://mongoc.org/libmongoc/current/
https://esp32io.com/tutorials/esp32-mysql

## Slide 146
CONNECTING TO MONGODB USING PYTHON
(Code added in Code Section)

## Slide 147
Steps:
Run the following commands and then use the code provided in Code Section and run it
$ sudo apt-get update
$ sudo python3 -m pip install pymongo
$ python3 -m pip install "pymongo[srv]"

## Slide 149
INSERTING MONGODB DOCUMENTS USING PYTHON
(Code added in Code Section)

## Slide 153
Connecting MongoDB with ESP32
https://www.mongodb.com/developer/how-to/create-data-api-10-min-realm/
https://jimb-cc.medium.com/esp-and-mongodb-sitting-in-a-tree-7d043fb1a4d
Code Added in Codes Section
Steps to be followed to connect to MongoDB Atlas from Realm are given in following slides
Results are added at the end

## Slide 154
Steps to connect to Atlas using Realm service

## Slide 155
Step 1: Deploy a Free Tier Cluster
Step 2: Create Database and collections inside that database
Step 3: open realm
Step 4: Add a Realm Service by clicking “Create a New App”

## Slide 156
Cluster name which we want to connect

## Slide 157
After adding ,the below option must be like this so that side menu appears
Step 5: Add Function:

## Slide 158
The function used is added in next slide
Change settings as follows(Leave the rest as it is):

## Slide 159
/*****Function1***************/
exports = function(payload) {
const mongodb = context.services.get("mongodb-atlas");
// change database_name and collection_name
const mycollection = mongodb.db("database_name").collection("collection_name");
return mycollection.find({}).limit(10).toArray();
};
/*****************Function2****************/
exports = function(payload){
var atlas = context.services.get("mongodb-atlas");
// change database_name and collection_name
var coll = atlas.db("database_name").collection("collection_name");
try {
if (payload.body)
{
//const ts = {ts:new Date()};
//const ts_ej = EJSON.stringify(ts);
body = EJSON.parse(payload.body.text());
body['ts'] = new Date();
}
coll.insertOne(body);
console.log(body);
} catch (e) {
console.log("Error inserting doc: " + e);
return e.message();
}
};

## Slide 160
Save draft and then review and deploy

## Slide 161
Step 6: Add Http Endpoint:

## Slide 162
COPY URL

## Slide 163
Choose Function name here
Save changes and deploy

## Slide 164
Arduino Code is Provided in Code section of this PPT
After running the code in ESP32 we got the following Results

## Slide 166
Collection : “Lock_Data”

## Slide 167
There are separate document corresponding to each tag. Each document has 2 fields:
Tag_id : It contains the Tag id of Tag
Lock_Status: This is stored as “1” to lock the Tag and as “0” to unlock it

## Slide 169
BUS_INFO

## Slide 170
A sample document in Bus Data Collection

## Slide 174
Option selected for plotting
Plotting Done every minute
MAX

## Slide 175
Cluster 0
ASSET_INFO
BUS_INFO
New Luggage Data
Employee Data
Lock_Status
OTP_Data
BUS Data

## Slide 176
HTTP Response codes
Status code | Meaning
1xx Informational | 
100 | Continue
101 | Switching protocols
102 | Processing
103 | Early Hints
2xx Succesful
200 OK
201 Created
202 Accepted
203 Non-Authoritative Information
204 No Content
205 Reset Content
206 Partial Content
207 Multi-Status
208 Already Reported
226 IM Used

## Slide 177
3xx Redirection | 
300 | Multiple Choices
301 | Moved Permanently
302 | Found (Previously "Moved Temporarily")
303 | See Other
304 | Not Modified
305 | Use Proxy
306 | Switch Proxy
307 | Temporary Redirect
308 | Permanent Redirect
4xx Client Error | 
400 | Bad Request
401 | Unauthorized
402 | Payment Required
403 | Forbidden
404 | Not Found
405 | Method Not Allowed
406 | Not Acceptable
407 | Proxy Authentication Required
408 | Request Timeout
409 | Conflict
410 | Gone
411 | Length Required
412 | Precondition Failed
413 | Payload Too Large
414 | URI Too Long
415 | Unsupported Media Type
416 | Range Not Satisfiable
417 | Expectation Failed
418 | I'm a Teapot
421 | Misdirected Request
422 | Unprocessable Entity
423 | Locked
424 | Failed Dependency
425 | Too Early
426 | Upgrade Required
428 | Precondition Required
429 | Too Many Requests
431 | Request Header Fields Too Large
451 | Unavailable For Legal Reasons

## Slide 179
Importing data in MongoDB from a csv file

## Slide 180
Install mongodb : https://www.mongodb.com/try/download/community
Download database tools: https://www.mongodb.com/try/download/database-tools
Copy the files from downloaded folder to MongoDB location in computer:
C:\Program Files\MongoDB\Server\5.0\bin
Also copy the .csv file in this location

## Slide 181
Ensure the following settings

## Slide 182
Ensure the following settings
If your current IP is not added then add this to your Atlas by clicking on Add IP Address button and selecting your current IP

## Slide 183
To check your Password

## Slide 184
Now go to Database -> CMD line tools

## Slide 185
General Command:
mongoimport --uri mongodb+srv://shubham:<PASSWORD>@cluster0.zqakj.mongodb.net/<DATABASE> --collection <COLLECTION> --type <FILETYPE> --file <FILENAME>
For
Password shubham
Database BUS_DATA
Collection BUS_OBD_DATA
Filetype csv
Filename newobd2.csv
mongoimport --uri mongodb+srv://shubham:shubham@cluster0.zqakj.mongodb.net/BUS_INFO --collection BUS_OBD_DATA --type csv --file newobd2.csv –headerline
mongoimport --uri mongodb+srv://shubham:shubham@cluster0.zqakj.mongodb.net/BUS_INFO --collection BUS_OBD_DATA --type csv --file newobd2.csv --fields field1_name,field2_name …
mongoexport --uri mongodb+srv://shubham:<PASSWORD>@cluster0.zqakj.mongodb.net/<DATABASE> --collection <COLLECTION> --type <FILETYPE> --out <FILENAME>
This command didn’t work once, that time I just restarted laptop and connected to iiscwlan4….it worked

## Slide 186
Open cmd and go to location of bin in MongoDB : C:\Program Files\MongoDB\Server\5.0\bin
Type the command mentioned in last slide and hit enter

## Slide 188
How to export MongoDB collection to csv file

## Slide 190
Open Windows Power shell in admin mode:
Press win + x
Select windows power shell admin
In file browser make an empty csv file with name text.csv at
location of mongoexport i.e. C:\Program Files\MongoDB\Server\5.0\bin
Enter cd C:\
Enter following commands shown in picture to navigate to bin folder
Enter the command for exporting
  .\mongoexport --uri mongodb+srv://shubham:shubham@cluster0.zqakj.mongodb.net --db BUS_INFO --collection Bus_exp_Data --csv --out text.csv --fields lattitude,longitude

## Slide 191
OTP For Verification
APP
{Mob no}
Mongo DB
{Random OTP Generation }
Gateway
with GSM
SMS in User’s mobile number
OTP : xxxx
New Document in database
{
Mob : “xxx”
OTP : “xxx”
}
{Mob no, OTP}
{Mob no, OTP}
{OTP}
Mobile Data
Mobile Data
SMS
Verify Entered OTP from http response
{OTP}
(http response)

## Slide 192: APP Development
Apps will be built in MIT APP Inventor .
Conductor App will be communicating directly to Gateway and User App will get information from Cloud Database.
MIT APP Inventor:
  GUI for App development.
  No coding Required.
  Free to use

## Slide 193: App1(For interaction with database)
This app is able to insert new documents to Luggage_Data collection of ASSET_INFO database
It is also helpful for reading, updating values of fields of documents in the same database.

## Slide 198: User App
This app allows user to register and add an entry in collection “New_Luggage_data” of database “ASSET_INFO”.
Users are required to Scan QR code provided in Tags for registration with a valid id
After registration User gets connected to Database automatically and the monitoring screen is displayed in mobile
In case of any crash or something the user also has the option for directly connecting to database if they have already registered by choosing the connect option in App

## Slide 199
Screen 1

## Slide 200
Screen : Add_Entry

## Slide 204
Screen : Screen_Connect

## Slide 205
Screen : Screen_Mongo
To be improved

## Slide 208
Conductor APP

## Slide 214
Modifications

## Slide 215
Side Menu:
When clicked shows a few options for settings, help, etc
Home:
Navigates to home screen of app
Drop down menu:
Helps in selecting beacon number from a list which helps to avoid typing problem
Magnify :
When clicked shows the complete description of Query result. After getting that information, Conductor gets an option to remove that Tag_id entry from database.

## Slide 216
Side Menu options
Close menu Button
Remove Passenger Entry:
Used to remove Tag id Directly by asking Tag id
Your Account:
Provides Account information and options to update it
Sign out:
Navigates to the login screen
Remove Employee Account:
Used to remove Conductor Entry from database
Home:
Used to Navigate to Home Screen
Customer Service:
Provides details to contact to Customer care Service

## Slide 217
OBD SIMULATOR APP

## Slide 219
"100":"Continue","101":"Switching protocols","102":"Processing","103":"Early Hints“
"200":"OK","201":"Created","202":"Accepted","203":"Non-Authoritative Information","204":"No Content","205":"Reset Content","206":"Partial Content","207":"Multi-Status","208":"Already Reported","226":"IM Used"
"300":"Multiple Choices","301":"Moved Permanently","302":"Found Previously Moved Temporarily","303":"See Other","304":"Not Modified","305":"Use Proxy","306":"Switch Proxy","307":"Temporary Redirect","308":"Permanent Redirect"
"400":"Bad Request","401":"Unauthorized","402":"Payment Required","403":"Forbidden","404":"Not Found","405":"Method Not Allowed","406":"Not Acceptable","407":"Proxy Authentication Required","408":"Request Timeout","409":"Conflict","410":"Gone","411":"Length Required","412":"Precondition Failed","413":"Payload Too Large","414":"URI Too Long","415":"Unsupported Media Type","416":"Range Not Satisfiable","417":"Expectation Failed","418":"I'm a Teapot","421":"Misdirected Request","422":"Unprocessable Entity","423":"Locked","424":"Failed Dependency","425":"Too Early","426":"Upgrade Required","428":"Precondition Required","429":"Too Many Requests","431":"Request Header Fields Too Large","451":"Unavailable For Legal Reasons“
"500":"Internal Server Error","501":"Not Implemented","502":"Bad Gateway","503":"Service Unavailable","504":"Gateway Timeout","505":"HTTP Version Not Supported","506":"Variant Also Negotiates","507":"Insufficient Storage","508":"Loop Detected","510":"Not Extended","511":"Network Authentication Required"
http response codes(“response_code”: “description”)

## Slide 221
Modifications in APP (Till 05/05/2022)

## Slide 226
Non Scrollable Screen
Scrollable Screen

## Slide 227: Lock
Esp32
SERVO-MOTOR
Push Button
Breadboard
Jumper wires

## Slide 229
Servo motor’s power pin, ground pin and control pin is connected to Arduino’s 5v pin, ground pin and pin3
Push button pin connected through Arduino to breadboard
Connection
Working
When push button is pressed once it moves from 0 to 180 degree, again push button is pressed then it come back from 180 degree to 0 initial position.

## Slide 230: Ideas for lock
1
2

## Slide 231
#include<Servo.h>
Servo myservo; // create servo object to control a servo
#define servoPin 3 //~
#define pushButtonPin 2
int angle =0; // initial angle for servo
int angleStep =10;
const int minAngle = 0;
const int maxAngle = 180;
int buttonPushed =0;
void setup() {
Serial.begin(9600); // setup serial
myservo.attach(servoPin); // attaches the servo on pin 3 to the servo object
pinMode(pushButtonPin,INPUT_PULLUP);
Serial.println(" Servo Button ");
}
Code

## Slide 232
void loop() {
if(digitalRead(pushButtonPin) == LOW){
buttonPushed = 1;
}
if( buttonPushed ){
// change the angle for next time through the loop:
angle = angle + angleStep;
// reverse the direction of the moving at the ends of the angle:
if (angle <= minAngle || angle >= maxAngle) {
angleStep = -angleStep;
buttonPushed = 0;
}
myservo.write(angle); // move the servo to desired angle
Serial.print("Moved to: ");
Serial.print(angle); // print the angle
Serial.println(" degree");
delay(100);
}
}

## Slide 234
ESP32
Servo-motor
Box (servo-motor will be inside)
0 to 90 degree angular rotation
Power IN
Unlock
Locked

## Slide 235: Lock Circuit
Servo-motor
Lock
Arduino
Push button

## Slide 236: In unlock position

## Slide 237: In locked position

## Slide 238: Lock working video

## Slide 239: 22nd oct – 29th oct
Tried to learn :
Android studio for app development(coding).
JAVA
MIT APP Inventor for App development(GUI).
Completed:
Bluetooth communication app using a reference from internet using MIT App inventor.
(https://puravidaapps.com/btchat.php )

## Slide 240
Two way Bluetooth Chat App using MIT APP Inventor:
Title(Textbox)
Username (TextBox)
Connect (ListPicker)
Disconnect,Clear,Exit,Send (Buttons)
Message Box
Message or Information Box

## Slide 242
INITIALIZATION

## Slide 243
//User1 Connected

## Slide 247: Ble scanner app resources
http://www.martyncurrey.com/arduino-hm-10-and-app-inventor-2/#AI2
http://iot.appinventor.mit.edu/#/bluetoothle/bluetoothleintro

## Slide 250
OBD to DB9 Converter
CAN Bus Shield

## Slide 251
Supported Mode 01 PIDs
Mode =
00 – 0A for request and
40- 4A for response

## Slide 252
OBD2 connector - type A vs. B
In practice, you may encounter both the type A and type B OBD2 connector. Typically, type A will be found in cars, while type B is common in medium and heavy duty vehicles.
the two types share similar OBD2 pinouts, but provide two different power supply outputs (12V for type A and 24V for type B). Often the baud rate will differ as well, with cars typically using 500K, while most heavy duty vehicles use 250K (more recently with support for 500K).
To help physically distinguish between the two types of OBD2 sockets, note that the type B OBD2 connector has an interrupted groove in the middle. As a result, a type B OBD2 adapter cable will be compatible with both types A and B, while a type A will not fit into a type B socket.
A few things to note:
The OBD2 connector is near your steering wheel, but may be hidden behind covers/panels
Pin 16 supplies battery power (often while the ignition is off)
The OBD2 pinout depends on the communication protocol
The most common protocol is CAN (via ISO 15765), meaning that pins 6 (CAN-H) and 14 (CAN-L) will typically be connected

## Slide 253
What is the ISO 15765 standard?
ISO 15765 refers to a set of restrictions applied to the CAN standard (which is itself defined in ISO 11898). One might say that ISO 15765 is like "CAN for cars".
In particular, ISO 15765-4 describes the physical, data link layer and network layers, seeking to standardize the CAN bus interface for external test equipment. ISO 15765-2 in turn describes the transport layer (ISO TP) for sending CAN frames with payloads that exceed 8 bytes. This sub standard is also sometimes referred to as Diagnostic Communication over CAN (or DoCAN). See also the 7 layer OSI model illustration.
OBD2 can also be compared to other higher layer protocols (e.g. J1939, CANopen).

## Slide 254
The five OBD2 protocols
As explained above, CAN bus today serves as the basis for OBD2 communication in the vast majority of cars through ISO 15765.
However, if you're inspecting an older car (pre 2008), it is useful to know the other four protocols that have been used as basis for OBD2. Note also the pinouts, which can be used to determine which protocol may be used in your car.
ISO 15765 (CAN bus): Mandatory in US cars since 2008 and is today used in the vast majority of cars
ISO14230-4 (KWP2000): The Keyword Protocol 2000 was a common protocol for 2003+ cars in e.g. Asia
ISO9141-2: Used in EU, Chrysler & Asian cars in 2000-04
SAE J1850 (VPW): Used mostly in older GM cars
SAE J1850 (PWM): Used mostly in older Ford cars

## Slide 255
OBD2 parameter IDs (PID)
Why should you care about OBD2 data?
Mechanics obviously care about OBD2 DTCs (maybe you do too), while regulatory entities need OBD2 to control emission.
But the OBD2 protocol also supports a broad range of standard parameter IDs (PIDs) that can be logged across most cars.
This means that you can easily get human-readable OBD2 data from your car on speed, RPM, throttle position and more.
In other words, OBD2 lets you analyze data from you car easily - in contrast to the OEM specific proprietary raw CAN data.
In principle it is simple to log the raw CAN frames from your car. If you e.g. connect a CAN logger to the OBD2 connector, you'll start logging broadcasted CAN bus data out-the-box. However, the raw CAN messages need to be decoded via a database of conversion rules (DBC) and a suitable CAN software that supports DBC decoding (like e.g. asammdf). The challenge is that these CAN DBC files are typically proprietary, making the raw CAN data unreadable unless you're the automotive OEM.
Car hackers may try to reverse engineer the rules, though this can be difficult. CAN is, however, still the only method to get "full access" to your car data - while OBD2 only provides access to a limited subset of data.

## Slide 256
How to log OBD2 data?
OBD2 data logging works as follows:
You connect an OBD2 logger to the OBD2 connector
Using the tool, you send 'request frames' via CAN
The relevant ECUs send 'response frames' via CAN
Decode the raw OBD2 responses via e.g. an OBD2 DBC
In other words, a CAN logger that is able to transmit custom CAN frames can also be used as an OBD2 logger.
Note that cars differ by model/year in what OBD2 PIDs they support. For details, see our OBD2 data logger guide.

## Slide 257
Raw OBD2 frame details
To get started recording OBD2 data, it is helpful to understand the basics of the raw OBD2 message structure. In simplified terms, an OBD2 message is comprised of an identifier and data. Further, the data is split in Mode, PID and data bytes (A, B, C, D) as below.
Identifier: For OBD2 messages, the identifier is standard 11-bit and used to distinguish between "request messages" (ID 7DF) and "response messages" (ID 7E8 to 7EF). Note that 7E8 will typically be where the main engine or ECU responds at.
Length: This simply reflects the length in number of bytes of the remaining data (03 to 06). For the Vehicle Speed example, it is 02 for the request (since only 01 and 0D follow), while for the response it is 03 as both 41, 0D and 32 follow.
Mode: For requests, this will be between 01-0A. For responses the 0 is replaced by 4 (i.e. 41, 42, … , 4A). There are 10 modes as described in the SAE J1979 OBD2 standard. Mode 1 shows Current Data and is e.g. used for looking at real-time vehicle speed, RPM etc. Other modes are used to e.g. show or clear stored diagnostic trouble codes and show freeze frame data.
PID: For each mode, a list of standard OBD2 PIDs exist - e.g. in Mode 01, PID 0D is Vehicle Speed. For the full list, check out our OBD2 PID overview. Each PID has a description and some have a specified min/max and conversion formula.
The formula for speed is e.g. simply A, meaning that the A data byte (which is in HEX) is converted to decimal to get the km/h converted value (i.e. 32 becomes 50 km/h above). For e.g. RPM (PID 0C), the formula is (256*A + B) / 4.
A, B, C, D: These are the data bytes in HEX, which need to be converted to decimal form before they are used in the PID formula calculations. Note that the last data byte (after Dh) is not used.

## Slide 258
The 10 OBD2 services (aka modes)
There are 10 OBD2 diagnostic services (or modes) as described in the SAE J1979 OBD2 standard. Mode 1 shows Current Data and is used for looking at real-time parameters like vehicle speed, RPM, throttle position etc. Other modes are e.g. used to show/clear diagnostic trouble codes (DTCs) and show freeze frame data.
Manufacturers do not have to support all diagnostic services - and they may support modes outside these 10 services (i.e. manufacturer specific OBD2 services).

## Slide 259
Formula for actual value of data received from OBD
[0]
[6]
[7]
[3]
[4]
[5]
[1]
[2]
Received frame

## Slide 261
Data stored in Simulator program.
Data received from (simulator )ESP32 in other ESP32(CAN sender)

## Slide 264
Methods for communication with Car OBD
https://www.instructables.com/CAN-Bus-Sniffing-and-Broadcasting-with-Arduino/

## Slide 265
Method 1 : Directly connecting OBD CAN Bus pins to CAN Receiver
CAN-H (shield) <-----> CAN-high (OBD-II) CAN-L (shield) <-----> CAN-low (OBD-II)

## Slide 266
Method 2: Connecting OBD to DB9 Cable to CAN Sheild
+
+
₹1,499.00 + ₹1,158.00
https://www.amazon.in/gp/product/B07JR221MH/ref=ewc_pr_img_2?smid=A3OFE3UKIO43OW&psc=1
https://www.amazon.in/dp/B094ZJKVGK?ref_=cm_sw_r_cp_ud_dp_J9A2V2V6CB5JR22R5N3G

## Slide 267
Method 3: Use OBD II ELM327 Scanner
₹799.00
https://www.amazon.in/dp/B083LC9YTQ?ref_=cm_sw_r_cp_ud_dp_YJNJ0J2FVK1HPQ47N61X
Here either we can use the Bluetooth App provided by them to get OBD Data
Or
We can remove the Bluetooth module from scanner and use the UART pins to get data. This task has been implemented in the link given below:
https://www.youtube.com/watch?v=EG94t0rqag4

## Slide 273
GSM Tx –> Arduino Rx and GSM Rx –> Arduino Tx. Now connect the ground pin of Arduino to ground pin of gsm module
Note:- The problem with this connection is that, while programming Arduino uses serial ports to load program from the Arduino IDE. If these pins are used in wiring, the program will not be loaded successfully to Arduino. So you have to disconnect wiring in Rx and Tx each time you burn the program to Arduino. Once the program is loaded successfully, you can reconnect these pins and have the system working!
To avoid this difficulty, I am using an alternate method in which two digital pins of Arduino are used for serial communication. We need to select two PWM enabled pins of Arduino for this method. So I choose pins 9 and 10 (which are PWM enabled pins). This method is made possible with the SoftwareSerial Library of Arduino. Software Serial is a library of Arduino which enables serial data communication through other digital pins of Arduino. The library replicates hardware functions and handles the task of serial communication.
https://microcontrollerslab.com/gsm-module-interfacing-arduino-send-receive-sms/

## Slide 274
Once you open a serial monitor, make sure that ‘Both NL & CR’ option is selected!
Also the sim card we are using must support 2G Network, so that the module works.

## Slide 275
/*
Please Read GSM Module Sheild must read pdf before using the code
OR
visit https://lastminuteengineers.com/sim900-gsm-shield-arduino-tutorial/
*/

## Slide 276: TIME PLAN SUMMARY
Jan – Sept :
                Pre-study Phase and Study Phase task completion.
                Final selection of technology and components to be used for our Project.
                Experiments were performed with a similar product SEEK-IT from Panasonic to check the functionality and get a basic understanding of its working.
Oct – Nov :
                Learning of Basics to handle tools like MIT APP INVENTOR, MongoDB, ESP32 BLE communication, necessary for our Project.
                Imaginary Scenario Planning which could lead to failure of our product.
Dec – Jan :
              Building a mini working model of our project with a single beacon and single gateway.
              Performing Real-time experiments with that mini model in bus.
Feb – Mar :
              Building the final working product with multiple beacons and multiple gateways.
              Testing and modification of the final working model.

## Slide 277
Detailed Time Plan of Project
13th Jan – 7th May :
          Product Survey of currently available products was done and similar products was studied for features offered by them.
          Prepared a product comparison table related to the product survey.
          Performed market survey and prepared the questionnaire and framed question according to our product.
          Study the embedded system topics like Cortex M3/M4 pipeline, peripherals, simple interrupts
          Prepared a wish specification, features sheets our components.
          Prepared a Pre-Phase study report.
15th May – 30th Sept :
          Study the Project related papers.
          We searched the different types of methods(BLE, Wi-Fi, UWB) for our project and collected materials for all methods.
          We have studied BLE(Bluetooth Low Energy), Wi-fi and UWB(Ultra Wide Band) based asset tracking methods.
          We have compared the BLE based asset tracking method over Wi-Fi and UWB methods.
          Prepared the Study Phase report.
          We have ordered the already available asset tracking product(Panasonic Seekit) in the market, perform an experiment with that device and analyse its working behaviour in open space and inside the metal box.

## Slide 278
Detailed Time Plan of Project
1st Oct – 30th Nov :
          Learn Basic App development using MIT APP INVENTOR.
          Build a Bluetooth communication App for chatting between 2 devices.
          Learn basics of MongoDB database and MongoDB Atlas cloud platform.
          Create a Database for containing information of Assets.
          Build an App for performing simple tasks like addition, updation ,deletion in a database in MongoDB.
          Learn to establish BLE communication between two ESP32 modules.
          Learn to establish communication between ESP32 and MongoDB database.
          Build a document containing list of imaginary scenarios which could lead to failure of our System in real time.
1st Dec – 31st Dec :
          Build a system which would update any sensor value collected from ESP32 on MongoDB cloud and the value in cloud would be visible to an app.
          Build a mini working system of our project containing one beacon and one Gateway along with MongoDB cloud and 2 apps for user and conductor.
          Perform Real time experiment of our model in Bus.

## Slide 279
Detailed Time Plan of Project
1st Jan – 15th Feb:
          Find solution to problems listed in Imaginary scenario planning document and problems found in Bus experiment.
          Implementation of those solution to the mini working model of our project.
          Build Final System with multiple beacons and multiple gateways.
          Build Final apps for conductor and user.
15th Feb – 28th Feb:
          Perform Real time experiment in a Bus.
          List Problems Found if any.
          Find Solutions to those Problems.
1st March – 30th June:
          Modifications in working model.
          Demo.
          Thesis Submission.

## Slide 280: Esp32 as i-Beacon
#include "sys/time.h"
#include "BLEDevice.h"
#include "BLEUtils.h"
#include "BLEServer.h"
#include "BLEBeacon.h"
#include "esp_sleep.h"
#define GPIO_DEEP_SLEEP_DURATION 10 // sleep x seconds and then wake up
RTC_DATA_ATTR static time_t last; // remember last boot in RTC Memory
RTC_DATA_ATTR static uint32_t bootcount; // remember number of boots in RTC Memory
// See the following for generating UUIDs:
// https://www.uuidgenerator.net/
BLEAdvertising *pAdvertising; // BLE Advertisement type
struct timeval now;
#define BEACON_UUID "8ec76ea3-6668-48da-9866-75be8bc86f4d" // UUID 1 128-Bit (may use linux tool uuidgen or random numbers via https://www.uuidgenerator.net/)

## Slide 281: Esp32 as i-Beacon
void setBeacon() {
BLEBeacon oBeacon = BLEBeacon();
oBeacon.setManufacturerId(0x4C00); // fake Apple 0x004C LSB (ENDIAN_CHANGE_U16!)
oBeacon.setProximityUUID(BLEUUID(BEACON_UUID));
oBeacon.setMajor((bootcount & 0xFFFF0000) >> 16);
oBeacon.setMinor(bootcount & 0xFFFF);
BLEAdvertisementData oAdvertisementData = BLEAdvertisementData();
BLEAdvertisementData oScanResponseData = BLEAdvertisementData();
oAdvertisementData.setFlags(0x04); // BR_EDR_NOT_SUPPORTED 0x04
std::string strServiceData = "";
strServiceData += (char)26; // Len
strServiceData += (char)0xFF; // Type

## Slide 282: Esp32 as i-Beacon
strServiceData += oBeacon.getData();
oAdvertisementData.addData(strServiceData);
pAdvertising->setAdvertisementData(oAdvertisementData);
pAdvertising->setScanResponseData(oScanResponseData);
}
void setup() {
Serial.begin(115200);
gettimeofday(&now, NULL);
Serial.printf("start ESP32 %d\n", bootcount++);
Serial.printf("deep sleep (%lds since last reset, %lds since last boot)\n", now.tv_sec, now.tv_sec - last);
last = now.tv_sec;
// Create the BLE Device
BLEDevice::init("ESP32 as iBeacon");

## Slide 283: Esp32 as i-Beacon
// Create the BLE Server
BLEServer *pServer = BLEDevice::createServer(); // <-- no longer required to instantiate BLEServer, less flash and ram usage
pAdvertising = BLEDevice::getAdvertising();
BLEDevice::startAdvertising();
setBeacon();
// Start advertising
pAdvertising->start();
Serial.println("Advertizing started...");
delay(100);
pAdvertising->stop();
Serial.printf("enter deep sleep\n");
esp_deep_sleep(1000000LL * GPIO_DEEP_SLEEP_DURATION);
Serial.printf("in deep sleep\n");
}
void loop() {
}

## Slide 284: Connect to MongoDB using python and show status

## Slide 285
from pymongo import MongoClient
# pprint library is used to make the output look more pretty
from pprint import pprint
# connect to MongoDB, change the << MONGODB URL >> to reflect your own connection string
client = MongoClient("mongodb+srv://shubham:Shubham100@cluster0.zqakj.mongodb.net/ASSET_INFO?retryWrites=true&w=majority")
db=client.admin
# Issue the serverStatus command and print the results
serverStatusResult=db.command("serverStatus")
pprint(serverStatusResult)

## Slide 286: Insert data in Mongodb using PYTHON

## Slide 287
from pymongo import MongoClient
from random import randint
#Step 1: Connect to MongoDB - Note: Change connection string as needed
client = MongoClient("mongodb+srv://shubham:Shubham100@cluster0.zqakj.mongodb.net/ASSET_INFO?retryWrites=true&w=majority")
db=client.business
#Step 2: Create sample data
names = ['Kitchen','Animal','State', 'Tastey', 'Big','City','Fish', 'Pizza','Goat', 'Salty','Sandwich','Lazy', 'Fun']
company_type = ['LLC','Inc','Company','Corporation']
company_cuisine = ['Pizza', 'Bar Food', 'Fast Food', 'Italian', 'Mexican', 'American', 'Sushi Bar', 'Vegetarian']
for x in range(1, 501):
business = {
'name' : names[randint(0, (len(names)-1))] + ' ' + names[randint(0, (len(names)-1))] + ' ' + company_type[randint(0, (len(company_type)-1))],
'rating' : randint(1, 5),
'cuisine' : company_cuisine[randint(0, (len(company_cuisine)-1))]
}
#Step 3: Insert business object directly into MongoDB via insert_one
result=db.reviews.insert_one(business)
#Step 4: Print to the console the ObjectID of the new document
print('Created {0} of 500 as {1}'.format(x,result.inserted_id))
#Step 5: Tell us that you are done
print('finished creating 500 business reviews')

## Slide 288: ASSET_INFO UPDATE:
from pymongo import MongoClient
from random import randint
#Step 1: Connect to MongoDB - Note: Change connection string as needed
client = MongoClient("mongodb+srv://shubham:Shubham100@cluster0.zqakj.mongodb.net/ASSET_INFO?retryWrites=true&w=majority")
db=client.ASSET_INFO
# dictionary to be added in the database
record={
"title": "MongoDB and Python number 2"
}
# inserting the data in the database
rec = db.Luggage_data.insert_one(record)

## Slide 289: MONGODB and ESP32

## Slide 290
Secrets.h
const char* ssid = "Shubham saurav";
const char* password = "1.2.3.4.";
const char* serverName ="https://us-east-1.aws.data.mongodb-api.com/app/10minexample-fzdpe/endpoint/10minapi";
// "https://us-east-1.aws.data.mongodb-api.com/app/application-0-kokbp/endpoint/application0";
// -- Project -------------------------------------------
#define CLIENT "Office Acera" // Client ID for the ESP (or something descriptive "Front Garden")
#define TYPE "ESP32" // Type of Sensor ("Hornbill ESP32" or "Higrow" or "ESP8266" etc.)
// -- Other - Helpers ------------------------------------
URL copied from http Endpoint

## Slide 291
Sketch:
#include <Arduino.h>
#include <WEMOS_SHT3X.h>
#include <ArduinoJson.h>
#include <WiFi.h>
#include <HTTPClient.h>
#include "secrets.h"
const int SAMPLES= 10;
const int LDR_READ_PIN= 36;
const int MOIST_POWER_PIN= 26;
const int MOIST_READ_PIN= 39;
RTC_DATA_ATTR int bootCount = 0;
RTC_DATA_ATTR char name[15] = CLIENT;
SHT3X sht30(0x45);
StaticJsonDocument<500> doc;
void setup()
{
pinMode(LED_BUILTIN, OUTPUT);
Serial.begin(115200);
digitalWrite(LED_BUILTIN, HIGH);
Serial.print("Connecting to ");
Serial.print(ssid);
Serial.print(" with password ");
Serial.println(password);
WiFi.begin(ssid, password);
while(WiFi.status() != WL_CONNECTED) {
delay(500);
Serial.print("."); }
Serial.println("");
Serial.print("Connected to WiFi network with IP Address: ");
Serial.println(WiFi.localIP());
digitalWrite(LED_BUILTIN, LOW); }

## Slide 292
void POSTData()
{
if(WiFi.status()== WL_CONNECTED){
HTTPClient http;
http.begin(serverName);
http.addHeader("Content-Type", "application/json");
String json;
serializeJson(doc, json);
Serial.println(json);
int httpResponseCode = http.POST(json);
Serial.println(httpResponseCode);
}
}
void getDevice()
{esp_sleep_wakeup_cause_t wakeup_reason;
wakeup_reason = esp_sleep_get_wakeup_cause();
uint64_t chipid=ESP.getEfuseMac();//The chip ID is essentially its MAC address(length: 6 bytes).
Serial.printf("***ESP32 Chip ID = %04X%08X\n",(uint16_t)(chipid>>32),(uint32_t)chipid);//print High 2 bytes
char buffer[200];
sprintf(buffer, "%04X%08X",(uint16_t)(chipid>>32),(uint32_t)chipid);
doc["device"]["IP"] = WiFi.localIP().toString();
doc["device"]["RSSI"] = String(WiFi.RSSI());
doc["device"]["type"] = TYPE;
doc["device"]["name"] = name;
doc["device"]["chipid"] = buffer;
doc["device"]["bootCount"] = bootCount;
doc["device"]["wakeup_reason"] = String(wakeup_reason); }

## Slide 293
void loop()
{
++bootCount; // move this to setup()
digitalWrite(LED_BUILTIN, HIGH);
getDevice();
senseLight(LDR_READ_PIN);
senseMoisture(MOIST_POWER_PIN, MOIST_READ_PIN);
senseTemp();
senseHumid();
digitalWrite(LED_BUILTIN, LOW);
delay(10000);
Serial.println("Posting...");
POSTData();
serializeJsonPretty(doc, Serial);
Serial.println("\nDone.");
}
Rest Functions not added here

## Slide 299: Points Discussed:
If luggages are placed one above another then the gateway might not even detect the bottom tags. So we have to come up with an idea that will allow our tags to get detected even in that condition.
One possible method is to use Tx power. Increase Tx power if beacon is unable to connect, we will increase the Tx power and keep on increasing till we find optimum power. In this case the alarm will be triggered only when beacon is unable to communicate with gateway.
We may be having mixture of both Active and Passive tags.
To find out cost of Passive tags.